## Slide 1: Attack, Detection and Countermeasures: A demo on Satellite Networks Security
Dr. Cesare Roseti, Ing. F. Belli and Prof. M. Luglio
CRESM- research unit of University of Rome “Tor Vergata”
Notes: -Quello che siamo per presentare è un caso di attacco in una rete satellitare che sfrutta la vulnerabilità che scaturisce dall’utilizzo dei PEP.
- Ma prima di tutto fornirò qualche dettaglio aggiuntivo sullo scenario e sulla necessità di utilizzare i PEP nel caso in cui il segmento satellitare è interconnesso a reti terrestri

## Slide 2: Reference scenario
Star-based architecture
DAMA to access return link
  CRA
  RBDC
  VBDC
User terminals run TCP/IP applications
Most of apps requires reliability
  TCP Connections towards remote servers
Notes: - Nell’individuazione di uno scenario di riferimento, si è cercato di coinvolgere tecnologie e architetture diffuse nei sistemi satellitari commerciali.
Il sistema satellitare è basato sullo standard DVB-RCS, in cui un insieme di terminali satellitari sono connessi ad una gateway mediante un’architettura a stella.
E’ importante sottolineare che l’accesso al canale di ritorno è basato su algoritmi di assegnazione di banda su domanda.
Da un lato ogni terminale satellitare rappresenta il punto d’accesso al satellite per una sotto-rete terreste
mentre la gateway fornisce un’interfaccia verso Internet dove si possono immaginare diversi server remoti

## Slide 3: TCP over DVB-RCS: issues
TCP transmission is ACK-clocked
  The higher is RTT the slower is througput increase
  Start up sending very slow
  Underutilization of the available resources
DAMA algorithms may introduce variable contributions to the overall RTT
  Further slow down of the bw probing
  Misleading signals of network concestion
A performance overview
TCP transmission scheduling
Throughput trends

## Slide 4: TCP Acceleration

## Slide 5: PEP vulnerability
PEPs terminate conns, grab all TCP packets (in plain text) and re-route them in new connections
  TCP PEP are not compatible with IPsec  Lost of confidentiality on PEP
  Maliciously changing routing rules, TCP packet can be dropped after ACK transmission  Lost of reliability of TCP!
SYN
SYN-ACK
ACK
Connection OK
Connection OK
Transfer completed
Connection Timeout

## Slide 6: Intrusion Detection System
1. Monitor SYN and FIN record
2. Monitor bytes over TCP conns
2. Monitor bytes over TCP conns
3. Collect Data from probes
4. Combine data from probes <#SYN,byte1,byte2>
5. Run Alarm
6. Run Remediation
7. Disable PEP
7. Disable PEP
8. Fix problem and enable PEP
8. Fix problem and enable PEP

## Slide 7: IDS goal
Risk reduction!!!!
Risk definition (Re): source-unaware traffic dropping
P(e): Likelihood of the event
V(e): PEP adoption
D(e): Lost of data/Denial of Service
Reduction of these factors

## Slide 8: DEMO presentation
DEMO through a Satellite Network Emulator Platform
  Reproduction of a DVB-RCS-like network
  DAMA over return link; NCC functionalities
  TCP client connected to Satellite terminal
  TCP server beyond Satellite Gateway
TCP Client
PEP
GEO
PEP
TCP Server
TCP Client
Malicious User
Packet Dropping
TCP Client
TCP Server
GEO
Time
Start FTP upload
Start attack
Manual attack detection
Early remediation
Ordinary operations
Attack
Detection
Remed.

## Slide 9: Move to emulator….

## Slide 10: Result analysis